## Slide 1: Trails That Last: Siting, Construction, and Maintenance
Logan-Park.org | Illinois Horse Fair

## Slide 2: First, Thanks.
You, for joining us today
  Please ask questions as we go, don’t wait
Sheryl King, Ph.D.
David Nobbe, Ph.D.
Emi Hayashi, D.V.M.

## Slide 3: Who I Am
Southern Ohio
Xenia
Virginia Tech
SIU Forestry

## Slide 4: Today’s Goal
Sensible trail work
Measure twice, cut once
Evidence-based techniques

## Slide 5: Why We Do It
Safety
Quality experience
Resource protection
Get more people riding

## Slide 7
In racing, this is awesome.
From a trail maintenance perspective,
this is a complete disaster.

## Slide 8: Why Trail Science Matters

## Slide 9: So, A Good Trail--
Protects you
Protects horses
Protects resources
Interesting

## Slide 10: Discussion – When Trails Fail You…
How do they fail you?
What are the most common problems that tick you off?

## Slide 11: Prep: Measure Twice, Cut Once

## Slide 12: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Rules
Regulations
Land ownership
Liability exposure

## Slide 13: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Power Equipment
Tractor w/ scoop & blade or
Dingo

## Slide 14: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Power Equipment
Tractor w/ scoop & blade or
Dingo

## Slide 15: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Power Equipment
Tractor w/ scoop & blade or
Other narrow-gauge mech

## Slide 16: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Clinometer

## Slide 17: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Clinometer
Image: extension.umn.edu

## Slide 18: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Clinometer
Never trust your eyeballs regarding slope!

## Slide 19: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Rock bar
Image: fhwa.dot.gov

## Slide 20: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Pulaski
Images: dedavisart.wordpress.com

## Slide 21: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Arborist telescoping loppers
  Keep you safely in the saddle
Image: atraes.com.au

## Slide 22: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Council rake
Image: amleo.com

## Slide 23: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Rogue hoe
Image: thestgeorgeco.com

## Slide 24: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Brushcutter
Image: freewtc.com

## Slide 25: Prep: Measure Twice, Cut Once
Tools
Tools
Time
Labor
Hand Equipment
Stump grubber

## Slide 27: Siting (designing the trail)

## Slide 28: Siting: Landform Position
Ridge
Valley
Sidehill
Best vistas
Most exposed
Fastest damaged (weather)
Hard to drain
Much braiding

## Slide 29: Siting: Landform Position
Ridge
Valley
Sidehill
Few vistas
Least exposed
Fastest damaged (mud)
Impossible to drain
Standing water health problems
Much braiding

## Slide 30: Siting: Landform Position
Ridge
Valley
Sidehill
Moderately exposed
Good vistas
Easy to drain
Minimal braiding
“Contour trail”
Rolling grade dips
Image: fs.fed.us

## Slide 31: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Landform slope
Higher is better

## Slide 32: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Landform slope
Trail slope
Lower is better
  5% to 8% max
  Less than you think!

## Slide 33: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Landform slope
Trail slope
Lower is better
  5% to 8% max
  Less than you think!
Contour trail

## Slide 34: Contour Trail Looks Like:

## Slide 35: Contour Trail Looks Like:

## Slide 36: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Old way: Half rule
“trail slope always less
than half landform slope”

## Slide 37
Image: fhwa.gov

## Slide 38: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Trail – Slope Alignment Angle
  (0 – 90°)
  Higher is better
  Hill’s facing (“aspect”)
  Trail’s direction
  65 to 90° ideal

## Slide 40: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Mineral Soil:
  Coarse
  Sand
  Silt
  Clay

## Slide 41: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
In loess, remove down to mineral soil
Add mixed fines
  Not graded

## Slide 42: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Trees
  Shield from rain
  Keep poor-draining trails wet

## Slide 43: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Trees
  Shield from rain
  Keep poor-draining trails wet
Grasses
  Resistant and resilient
  Browse, ticks

## Slide 44: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Do you have to share the trail?

## Slide 45: Safer Shared Trails

## Slide 46
Motorized recreation

## Slide 47
Motorized recreation
Physical buffer

## Slide 48
Motorized recreation, road cyclists
Physical buffer
Hikers and MTB bikers

## Slide 49
Motorized recreation, road cyclists
Physical buffer
Hikers and MTB bikers
See-through fence, below 54 inches

## Slide 50: Pro tip: Use fire to manage for wildlife, Use well-planned trail as fire line

## Slide 51: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
High maintenance trails look like this:
Image: elibrary.dep.state.pa.us

## Slide 52: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Low maintenance trails look like this:
Image: fhwa.dot.gov

## Slide 53: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Low maintenance trails look like this:
Image: fhwa.dot.gov

## Slide 54: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Low maintenance trails look like this:
Image: fhwa.dot.gov

## Slide 55: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Trails parallel to streams become streams
50 – 150 ft. buffer to waterways based on slope

## Slide 56: Siting: Set the Centerline
Slope
TSA
Substrate
Vegetation
Use level and type
Water
Sight lines
Not so good:
Image: woodlandstewardship.org

## Slide 57: Trail Construction
Image: chattanoogahiking.com

## Slide 58: Safety First and Last
The only good trail work day is one without spurting head wounds
Know your “kill radius”

## Slide 59: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation

## Slide 60: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation

## Slide 61: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
Images: fs.fed.us
This
2 – 5% outslope

## Slide 62: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
Images: fs.fed.us
This
Not this

## Slide 63: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
High-lining icebergs in/out

## Slide 64: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
Image: fhwa.dot.gov

## Slide 65
Compacted subgrade
(mineral soil)

## Slide 66
Compacted subgrade
(mineral soil)
12 inches compacted aggregate subbase

## Slide 67
Compacted subgrade
(mineral soil)
12 inches compacted aggregate subbase
2 inches compacted aggregate base course

## Slide 68
Compacted subgrade
(mineral soil)
12 inches compacted aggregate subbase
2 inches compacted aggregate base course
2 inches compacted aggregate surface course

## Slide 69
Compacted subgrade
(mineral soil)
12 inches compacted aggregate subbase
2 inches compacted aggregate base course
2 inches compacted aggregate surface course
Have a friend with a dump truck (16 cubic yards) or a souped-up tractor + hauling trailer

## Slide 70: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
Aggressively clear for safety and sight lines, but no more

## Slide 71: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
Aggressively clear for safety and sight lines, but no more
Leave as many trees intact as possible

## Slide 72: Trail Construction
Flag
Cut
Subsurface
Surface
Vegetation
Aggressively clear for safety and sight lines, but no more
Leave as many trees intact as possible
Cross large trees on the uphill side

## Slide 73
Image: for.gov.bc.ca

## Slide 74
Image: for.gov.bc.ca
10 ft. minimum, 12 ft. safer

## Slide 75
Limbing

## Slide 76
Limbing
Brushing

## Slide 77
Limbing
Brushing
Stump grubbing

## Slide 78: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Image: fhwa.dot.gov

## Slide 79: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Image: Humane Society

## Slide 80: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Cut back vegetation

## Slide 81: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Cut back vegetation
Reassurance markers
Image: woodlandsteward.com

## Slide 82: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Cut back vegetation
Reassurance markers
Wayfinding

## Slide 83: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Cut back vegetation
Reassurance markers
Wayfinding
Closing visitor-created trails

## Slide 85: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Cut back vegetation
Reassurance markers
Wayfinding
Closing visitor-created trails
Mitigating standing water

## Slide 86: Trail Maintenance
Late winter
As needed
Following storms
De-berming
Removing pest wildlife
Cut back vegetation
Reassurance markers
Wayfinding
Closing visitor-created trails
Mitigating standing water
Spook hazards

## Slide 87: Success Stories – Shawnee National Forest
7 federally designated wilderness areas near
Image: fs.fed.us

## Slide 88: Success Stories – Shawnee National Forest
7 federally designated wilderness areas near
10 riding areas
Image: blogspot.com

## Slide 89: Success Stories – Shawnee National Forest
7 federally designated wilderness areas near
10 riding areas
Top-ranked trail volunteer coordinator in the country
Image: thesouthern.com

## Slide 90: Success Stories – Shawnee National Forest
7 federally designated wilderness areas
10 riding areas
Top-ranked trail volunteer coordinator in the country
Multiple horse-friendly campgrounds nearby
Image: fs.usda.gov

## Slide 91: Success Stories – Acadia National Park
Image: usparks.about.com

## Slide 92
Image: acadiamagic.com

## Slide 93: Success Stories – Acadia National Park
Image: exploringtheusbyrv.com

## Slide 94
Image: exploringtheusbyrv.com

## Slide 95: Other Success Stories?
Where have you been that rode really well?

## Slide 96: Handy Resources
Equestrian Trail Design Guidebook
  links.logan-park.org/index.php/?i=16
Professional Trail Builders Association
  ptba.org
U.S.F.S. Trail Construction Manual
  links.logan-park.org/index.php/?i=17
Shawnee Trail Conservancy
  shawneetrailconservancy.com
Equestrian Trail BMPs
  http://links.logan-park.org/index.php/?i=19

## Slide 97: Thank You Again
Questions and comments?